## Slide 1: ietf-ccamp-yang-otn-slicing
GitHub: https://github.com/aguoietf/ietf-ccamp-yang-otn-slicing
Document format
  Propose to use Kramdown for easily tracking changes
  .txt, .docx versions also uploaded

## Slide 2: Issue Tracking
https://github.com/aguoietf/ietf-ccamp-yang-otn-slicing/issues

## Slide 3: Proposed Call Schedule
Weekly or Bi-weekly
Candidate time slots
  Doodle poll: https://doodle.com/poll/8eb8iabyhx2vewyi
    Tue 10-11am EST / 10-11pm China / 4-5pm Europe
    Wed 8-10am EST / 8-10pm China / 2-4pm Europe
    Thu 9-10am EST/ 9-10pm China / 3-4pm Europe
    Fri 8-10am EST / 8-10pm China / 2-4pm Europe

## Slide 4: Functional Diagram of OTN-SC
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI
Reference to the other draft

## Slide 5: OTN-SC Deployment Scenarios
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI

## Slide 6: Expanded View of OTN-SC
OTN-SC
OTN-SC
L-MDSC
OTN-SC
PNC
PNC
PNC
Non-recursive (OTN-SC),
Multi-domain recursive (MPI)
Recursive (OTN-SC),
Multi-domain recursive (MPI)
Non-recursive,
Single domain
MPI
MPI
MPI
MPI
NBI
NBI
NBI
IETF-NSC
Notes: Use case 1 : realization of IETF NSC at optical layer
Use case 2 : realization of IETF NSC is to use existing OTN slices to

## Slide 7: OTN-SC Figure Update

## Slide 8: Issues - https://github.com/aguoietf/ietf-ccamp-yang-otn-slicing/issues

## Slide 9: Functional Diagram of OTN-SC
PNC
MPI
OTN-SC
IETF-NSC
OTN-SC NBI
Orchestrator/E2E SC
NSC NBI
OLD
NEW

## Slide 10: Scope of An OTN Slice
CE1
OTN PE1
OTN PE 2
CE2
OTN Slice
OTN Link
Access Link
Access Link
CE
OTN PE
OTN PE
CE
OTN Slice 1
OTN Link
Access Link
Access Link
OTN Border Node
OTN Border Node
OTN Slice 2
Single Domain
Multi Domain
End-to-end OTN Slice
Inter-domain OTN Link
OTN Link
OTN Domain 1
OTN Domain 2
X
Y
X
Y

## Slide 11: Multi-domain OTN-SC
OTN-SC
PNC
Single Domain
MPI
OTN-SC
L-MDSC
PNC
MPI
MPI
PNC
Multi Domain Option 1
OTN-SC
OTN-SC
OTN-SC NBI
Multi Domain Option 2
OTN-SC
PNC
PNC
MPI

## Slide 12: Draft-liu-teas-transport-network-slice-yang
draft-liu-teas-transport-network-slice-yang-04 (ietf.org)
module: ietf-network-slice
augment /nw:networks/nw:network/nw:network-types:
+--rw network-slice!
augment /nw:networks/nw:network:
+--rw network-slice
+--rw optimization-criterion? identityref
+--rw delay-tolerance? boolean
+--rw periodicity* uint64
+--rw isolation-level? identityref
augment /nw:networks/nw:network/nw:node:
+--rw network-slice
+--rw isolation-level? identityref
+--rw compute-node-id? string
+--rw storage-id? string
augment /nw:networks/nw:network/nt:link:
+--rw network-slice
+--rw delay-tolerance? boolean
+--rw periodicity* uint64
+--rw isolation-level? identityref

## Slide 13: Draft-wd-teas-transport-slice-yang
draft-liu-teas-transport-network-slice-yang-04 (ietf.org)
module: ietf-network-slice
+--rw network-slices
+--rw slice-templates
| +--rw slo-template* [id]
| +--rw id string
| +--rw template-description? string
+--rw network-slice* [network-slice-id]
+--rw network-slice-id uint32
+--rw network-slice-name? string
+--rw network-slice-tag? string
+--rw network-slice-topology* identityref
+--rw network-slice-slo-group* [slo-group-name]
| +--rw slo-group-name string
| +--rw default-slo-group? boolean
| +--rw (slo-template)?
| | +--:(standard)
| | | +--rw template? -> /network-slices/slice-templates/slo-template/id
| | +--:(custom)
| | +--rw network-slice-slo-policy
| | +--rw latency
| | | +--rw one-way-latency? uint32
| | | +--rw two-way-latency? uint32
| | +--rw jitter
| | | +--rw one-way-jitter? uint32
| | | +--rw two-way-jitter? uint32
| | +--rw loss
| | | +--rw one-way-loss? decimal64
| | | +--rw two-way-loss? decimal64
| | +--rw availability-type? identityref
| | +--rw isolation-type? identityref
| | +--rw network-slice-metric-bounds
| | +--rw network-slice-metric-bound* [metric-type]
| | +--rw metric-type identityref
| | +--rw upper-bound? uint64
| +--rw network-slice-member-group* [network-slice-member-id]
| | +--rw network-slice-member-id -> /network-slices/network-slice/network-slice-member/network-slice-member-id
| +--ro slo-group-monitoring
| +--ro latency? uint32
| +--ro jitter? uint32
| +--ro loss? decimal64
+--rw status
| +--rw admin-enabled? boolean
| +--ro oper-status? operational-type
+--rw network-slice-endpoint* [endpoint-id]
| +--rw endpoint-id uint32
| +--rw endpoint-name? string
| +--rw endpoint-role* identityref
| +--rw geolocation
| | +--rw altitude? int64
| | +--rw latitude? decimal64
| | +--rw longitude? decimal64
| +--rw node-id? string
| +--rw port-id? string
| +--rw network-slice-match-criteria
| | +--rw network-slice-match-criteria* [match-type]
| | +--rw match-type identityref
| | +--rw value? string
| +--rw endpoint-ip? inet:host
| +--rw bandwidth
| | +--rw incoming-bandwidth
| | | +--rw guaranteed-bandwidth? te-types:te-bandwidth
| | +--rw outgoing-bandwidth
| | +--rw guaranteed-bandwidth? te-types:te-bandwidth
| +--rw mtu uint16
| +--rw routing
| | +--rw bgp
| | | +--rw bgp-peer-ipv4* inet:ipv4-prefix
| | | +--rw bgp-peer-ipv6* inet:ipv6-prefix
| | +--rw static
| | +--rw static-route-ipv4* inet:ipv4-prefix
| | +--rw static-route-ipv6* inet:ipv6-prefix
| +--rw status
| | +--rw admin-enabled? boolean
| | +--ro oper-status? operational-type
| +--ro endpoint-monitoring
| +--ro incoming-utilized-bandwidth? te-types:te-bandwidth
| +--ro incoming-bw-utilization decimal64
| +--ro outgoing-utilized-bandwidth? te-types:te-bandwidth
| +--ro outgoing-bw-utilization decimal64
+--rw network-slice-member* [network-slice-member-id]
+--rw network-slice-member-id uint32
+--rw src
| +--rw src-network-slice-endpoint-id? -> /network-slices/network-slice/network-slice-endpoint/endpoint-id
+--rw dest
| +--rw dest-network-slice-endpoint-id? -> /network-slices/network-slice/network-slice-endpoint/endpoint-id
+--rw monitoring-type? network-slice-monitoring-type
+--ro network-slice-member-monitoring
+--ro latency? uint32
+--ro jitter? uint32
+--ro loss? decimal64

## Slide 14: Modeling for OTN Slices
2-in-1:
Build a topology
  Single-node for connectivity-based slices
  Multi-node/link topology for resource-based slices
Create connectivity on the topology
  Mandatory for connectivity-based slices
  Optional for resource-based slices

## Slide 15: Modeling for Connectivity-based OTN Slices
Option 1: single-node topology
  Endpoint list
    Each endpoint has:
      Endpoint id
      Reference to PE LTP
      (Optional) Resource id (time slot, VLAN ids etc.)
  Connectivity matrix - p2p connectivity between endpoints
    Committed: resource is activated
    Uncommitted: resource is reserved but not activated
    Default behavior of connectivity matrix
Node
EP1
EP2
EP3
EP4
Connectivity

## Slide 16: Modeling for Connectivity-based OTN Slices
Option 2: edge-edge topology
  Endpoint list
    Each endpoint has:
      Endpoint id
      Reference to PE LTP
      (Optional) Resource id (time slot, VLAN ids etc.)
  Connectivity matrix - p2p connectivity between endpoints
    Committed: resource is activated
    Uncommitted: resource is reserved but not activated
    Default behavior of connectivity matrix
    Path associated with a p2p connection
Node2
EP1
EP2
EP3
EP4
Link1
Node1
TP1
TP3
Link2
TP2
TP4
path

## Slide 17: Modeling for Resource-based OTN Slices
Full topology
  Endpoint list
    Each endpoint has:
      Endpoint id
      Reference to PE LTP
      (Optional) Resource id (time slot, VLAN ids etc.)
  SLOs
    SLOs for network, link, node and TP
  Connectivity matrix - p2p connectivity between endpoints
    Committed: resource is activated
    Uncommitted: resource is reserved but not activated
    Default behavior of connectivity matrix
    Path associated with a p2p connection
Node2
EP1
EP2
EP3
EP4
Link1
Node1
TP1
TP3
Link2
TP2
TP4
Node3
TP5
EP5
Link3

## Slide 18: Base Model for Slicing
Base model should be technology-agnostic
  Network slice as a topology
  Connectivity matrix
  Technology-agnostic SLO policies
    slice, node, link, TP (endpoint), connection (in connectivity matrix)
Base model candidates
  draft-liu-teas-transport-network-slice-yang
    Define connectivity matrix
    Define endpoints (mark access TPs as endpoints?)
    Define SLO for endpoint and connections
  draft-ietf-teas-actn-vn-yang
    Remove “ACTN” in the title
    Disentangle with TE topology
      Move SLO definitions to VN from TE connectivity matrix
      Remove steps for VN compute
  draft-ietf-teas-ietf-network-slice-nbi-yang
    Missing support resource-based slicing (partitioning)
    SLOs are packet-specific

## Slide 19: How do we merge these candidate base models?
VN + draft-liu ?
  Define VN as a network topology (rename VN as “slice” ? )
  Keep the definition of AP and VN-AP (maybe align with the “endpoint” naming)
    AP points to TPs in the topology
  Keep vn-member (rename it as “connectivity matrix” ?)
    Underlay path pointing to set of links/tps in network topology
  Define technology-agnostic SLO policies
    vn, node, link, TP (endpoint), connection (in connectivity matrix)
module: ietf-vn
+--rw access-point
| +--rw ap* [ap-id]
| +--rw ap-id ap-id
| +--rw vn-ap* [vn-ap-id]
| +--rw vn-id? -> /virtual-network/vn/vn-id
| +--rw vn-ap-id ap-id
| +--rw vn-node -> /virtual-network/vn/vn-topology/node/node-id
| +--ro vn-ap-slo
+--rw network-topology
| +--rw topology* [topology-id]
| +--rw topology-id
| +--rw node [node-id]
| | +--rw slo
| +--rw link [link-id]
| | +--rw slo
| +--rw tp [tp-id]
| +--rw slo
+--rw virtual-network
+--rw vn* [vn-id]
+--rw vn-id vn-id
+--rw vn-topology-id ->/network-topology/topology/topology-id
+--rw vn-member* [vnm-id]
| +--rw src vn-ap
| +--rw dst vn-ap
| +--rw underlay-path
| +--rw slo
+--rw slo

## Slide 20: How do we merge these candidate base models?
VN + draft-liu + draft-teas-ns
  Changing names
    VN – network slices
    Access point – endpoints
  Service mapping + VN = NS ?
module: ietf-vn
+--rw access-point
| +--rw ap* [ap-id]
| +--rw ap-id ap-id
| +--rw vn-ap* [vn-ap-id]
| +--rw vn-id? -> /virtual-network/vn/vn-id
| +--rw vn-ap-id ap-id
| +--rw vn-node -> /virtual-network/vn/vn-topology/node/node-id
| +--ro vn-ap-slo
+--rw network-topology
| +--rw topology* [topology-id]
| +--rw topology-id
| +--rw node [node-id]
| | +--rw slo
| +--rw link [link-id]
| | +--rw slo
| +--rw tp [tp-id]
| +--rw slo
+--rw virtual-network
+--rw vn* [vn-id]
+--rw vn-id vn-id
+--rw vn-topology-id ->/network-topology/topology/topology-id
+--rw vn-member* [vnm-id]
| +--rw src vn-ap
| +--rw dst vn-ap
| +--rw underlay-path
| +--rw slo
+--rw slo

## Slide 21: TEAS Interim Meeting on Network Slicing
Endpoints & scope of a network slice
|<---------------------- (1) ---------------------->|
| |
| |<-------------------- (2) -------------------->| |
| | | |
| | |<----------- (3) ----------->| | |
| | | | | |
| | | |<-------- (4) -------->| | | |
| | | | | | | |
V V AC V V V V AC V V
+-----+ | +-----+ +-----+ | +-----+
| |--------| | | |--------| |
| CE1 | | | PE1 |. . . . . . . . .| PE2 | | | CE2 |
| |--------| | | |--------| |
+-----+ | +-----+ +-----+ | +-----+
^ ^ ^ ^
| | | |
| | | |
Customer Provider Provider Customer
Edge 1 Edge 1 Edge 2 Edge 2
Figure 1 : Positioning IETF Network Slice Endpoints
(1) If the CE is operated by the IETF Network Slice service provider,
then the edge of the IETF Network Slice may be within the CE. In
this case the slicing process may utilize resources from within
the CE such as buffers and queues on the outgoing interfaces.
(2) The IETF Network Slice may be extended as far as the CE, to
include the AC, but not to include any part of the CE. In this
case, the CE may be operated by the customer or the provider.
Slicing the resources on the AC may require the use of traffic
tagging (such as through Ethernet VLAN tags) or may require
traffic policing at the AC link ends.
(3) In another model, the endpoints of the IETF Network Slice are the
customer-facing ports on the PEs. This case can be managed in a
way that is similar to a port-based VPN: each port (AC) or
virtual port (e.g., VLAN tag) identifies the IETF Network Slice
and maps to an IETF Network Slice endpoint.
(4) Finally, the endpoint of the IETF Network Slice may be within the
PE. In this mode, the PE classifies the traffic coming from the
AC according to information (such as the source and destination
IP addresses, payload protocol and port numbers, etc.) in order
to place it onto an IETF Network Slice.

## Slide 22: TEAS Interim Meeting on Network Slicing
Allowing for multiple connectivity matrices in a network slice
Consider the definition of connectivity matrix in the current draft and as discussed in issue #1. A consumer may want multiple connectivity matrices in their "contract" with the provider. In the example with four edge nodes (A, B, C, D), their may be traffic that flows between some edges, but not between others. For example, a consumer may want a slice that is ultra-low latency, and they may know that they want to send traffic from A to B, from A to C and multicast from D to A, B, and C. It is, of course, possible to express this as three separate slices. And this is perfectly acceptable. We must not make any definitions that prevent this from being the case. However, it seems likely that the consumer (and the operator) would prefer to talk about "the consumer's low latency slice". That is, to bundle these three connections into one construct. However, they are distinctly different connections and must be understood as such. Indeed, they may have some different SLOs associated (for example, A-B may require more bandwidth than A-C). By allowing (but not mandating) multiple connectivity matrices in a single slice service, we facilitate this administrative group. One could also imagine (but I do not pre-judge the network slice service YANG model definition) a default set of SLOs that apply to all connectivity matrices in a slice, and specific modified SLOs per connectivity matrix. Now, to Igor's point. This is about how traffic arriving at an edge (say a PE) is mapped to the correct connection. I promised a Venn diagram, but words are easier If we take the model of a port-based VPN, then one approach might be to map the (virtual or physical) port number or VLAN ID to the network slice. But clearly (and this was Igor's point) this doesn't identify the connectivity matrix if there is more than one matric per slice. A solution I offered is that the VLAN ID could identify {slice, connectivity matrix}. At that PE, for a given AC to a CE, it is necessary to expose with a separate VLAN ID for each {slice, connectivity matrix}. That does not mean: - we need a global unique identifier for each connectivity matrix - we need a per-PE unique identifier for each connectivity matrix

## Slide 23: TEAS Interim Meeting on Network Slicing
Realization architecture and “filter topology”
-- -- --
|CE| |CE| |CE|
-- -- --
AC : AC : AC :
---------------------- -------
( |PE|....|PE|....|PE| ) ( IETF )
( --: -- :-- ) ( Network )
( :............: ) ( Slice )
( IETF Network Slice ) ( ) Customer
---------------------- ------- View
........................\........./..................
\ / Controller
>>>>>>>>>>>>>>> Grouping/Mapping v v View
^ -----------------------------------------
^ ( |PE|.......|PE|........|PE|.......|PE| )
------------ ( --: -- :-- -- )
| | ( :...................: )
| Controller | ( Network Resource Partition )
| (NSC) | -----------------------------------------
| | |
| |>>>>> Resource Partitioning |
------------ of Available Topology |
v v v
v v ----------------------------- --------
v v (|PE|..-..|PE|... ..|PE|..|PE|) ( )
v v ( :-- |P| -- :-: -- :-- ) ( Filter )
v v ( :.- -:.......|P| :- ) ( Topology )
v v ( |P|...........:-:.......|P| ) ( )
v v ( - Filter Topology ) --------
v v ----------------------------- A
v >>>>>>>>>>>> Topology Filter A /
v .......................\............../..............
v \ / Physical Network
v ------------------------------------------------
v ( |PE|.....-.....|PE|....... |PE|.......|PE| )
v ( -- |P| -- :-...:-- -..:-- )
>>>>>>>>>( : -:..............|P|.........|P| )
( -.......................:-:..- - )
( |P|..........................|P|......: )
( - - )
------------------------------------------------
The Physical Network may be filtered into a number of Filter Topologies. Filter actions may include selection of specific nodes and links according to their capabilities and are based on network- wide policies. The resulting topologies can be used to host IETF Network Slices and provide a useful way for the network operator to know that all of the resources they are using to plan a network slice meet specific SLOs. This could be an offline planning activity or could be performed dynamically as new demands arise.
The use of Filter Topologies is entirely optional in the architecture and IETF Network Slices could be hosted directly on the Physical Network.

## Slide 24: Generic Model Proposal (Xufeng’s Proposal)
augment /nw:networks/nw:network/nw:node:
+--rw te-node-id? te-types:te-node-id
+--rw te!
+--rw te-node-attributes
| +--rw admin-status? te-types:te-admin-status
| +--rw activated boolean <== augmentation
| +--rw connectivity-matrices
| | +--rw connectivity-matrix* [id]
| | +--rw id uint32
| | +--rw activated boolean <== augmentation

## Slide 25: Generic Model Proposal (VN+draft-liu)
module: ietf-ns-generic
+--rw access-point
| +--rw ap* [ap-id]
| +--rw ap-id ap-id //access point id (pre-negotiated between CE-PE)
| +--rw pe-node-id string //PE node identifier
+--rw network-slice* [ns-id]
+--rw ns-id string
+--rw ns-description string
+--rw customer-name* string
+--rw ns-type? identityref // type of network slice: type 1 or type 2
+--rw slo // SLO/SLE policy of the network slice
| +-- ...
+--rw network-topology //network topology (single-node, multi-node
| +--rw topology* [topology-id] // schema-mount of draft-liu?
| +--rw topology-id
| +--rw node [node-id]
| | +--rw slo
| +--rw link [link-id]
| | +--rw slo
| +--rw tp [tp-id]
| +--rw slo
| +--rw is-endpoint? Boolean
| +--rw ap-id? ->/access-point/ap/ap-id
+--rw connectivity-matrices
  +--rw connectivity-matrix* [connectivity-matrix-id]
  +--rw connectivity-matrix-id uint32
  +--rw network-topology-id ->/network-slice/network-topology/topology/topology-id
  +--rw src-endpoint ->/network-slice/network-topology/topology/tp/tp-id
  +--rw dst-endpoint ->/network-slice/network-topology/topology/tp/tp-id
  +--rw underlay-path[index]
  | +--rw index uint16
  | +--rw node-id ->/network-slice/network-topology/topology/node/node-id
  | +--rw tp-id ->/network-slice/network-topology/topology/tp/tp-id
  | +--rw slo
  +--rw slo