## Slide 1: Framework and Data Model for OTN Network Slicing
Co-authors:
Haomian Zheng (Huawei)
Italo Busi (Huawei) Aihua Guo (Futurewei)
Victor Lopez(Telefonica)
Contributors:
Henry Yu (Huawei)
draft-zheng-ccamp-yang-otn-slicing-01

## Slide 2: OTN Slicing Interfaces
OTN slice controller (OTN-SC) may be deployed either outside or within an SDN controller
  Translating slice configuration into OTN TE topology or TE tunnel requests at the MPI, or
  Interact with higher- or lower-level slice controller in a recursive manner
Interaction between OTN-SC and IETF network slice controller is for further study
  An IETF network slice controller may use an OTN-SC to provision OTN slices to support end-to-end slicing

## Slide 3: OTN Slicing Realization @ MPI
Connectivity-based
  An OTN slice is realized by creating client services over ODU switched TE tunnels.
  This case is already covered by existing YANG model clusters:
    Network topology/generic TE topology/OTN TE topology
    Generic TE tunnel/OTN TE tunnel
    Client signal
Resource-based
  Realizing an OTN slice by reserving ODU topological resources
  This is the focus of the YANG model proposed in this draft

## Slide 4: Major Updates since IETF 109
Added co-authors
Updated use case description
  Leased Line Services with OTN
  Co-construction and Sharing
  Wholesale of optical resources
  Vertical dedicated network with OTN
Added YANG data model for OTN-SC MPI
  OTN slice realization with ODU resource coloring over TE topology
    Link- or time slot-based
  ODU resource reservation is performed by the underlying PNC/MDSC

## Slide 5: YANG Model @ MPI
module: ietf-otn-slice
augment /nw:networks/nw:network/nt:link/tet:te/tet:te-link-attributes:
+--rw (otn-slice-granularity)?
+--:(link)
| +--rw slice-id? uint32
+--:(link-resource)
+--rw slices* [slice-id]
+--rw slice-id uint32
+--rw (technology)?
| +--:(otn)
| +--rw otn-ts-num? uint32
+--ro sliced-link-ref? -> ../../../../../nt:link/link-id
* A prior version of this YANG model was contributed to ONAP and is included in its Guilin Release.

## Slide 6: Next Steps
Add YANG data model for OTN-SC NBI
  Possible to augment the model defined by draft-liu-teas- transport-network-slice-yang-01
Address the slicing for external (access and inter-domain) links
Align with draft-ietf-teas-ietf-network-slice-definition on the terms and definitions
  New use case: OTN slicing is a realization of IETF network slice
Address comments and reviews from the WG
Socialize and invite more co-authors and contributors before a possible call for WG adoption

## Slide 7: New Use Cases for OTN Slicing
customer
Orchestrator
CMI: (customer’s) OTN slice request
OTN-SC
customer
Orchestrator
Other services
OTN-SC
E2E slice controller
NSC
OTN slice request
OTN slice request
PNC/MDSC
PNC/MDSC
MPI: TE tunnel/TE topo + slice id
E2e slice request
Network slice request
MPI: TE tunnel/TE topo + slice id
  Current use cases:
  Leased Line Services with OTN
  Co-construction and Sharing
  Wholesale of optical resources
  Vertical dedicated network with OTN
New use case
OTN slice is (part of) a realization of IETF network slice

## Slide 8
Thank You!