## Slide 1: Framework and Data Model for OTN Network Slicing
Co-authors:
Aihua Guo (Futurewei)
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Luis M. Contreras (Telefonica)
Yunbin Xu (CAICT)
Yang Zhao (China Mobile)
Xufeng Liu (IBM Corporation)
draft-ietf-ccamp-yang-otn-slicing-04
Contributors:
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Victor Lopez(Nokia)
Dieter Beller (Nokia)
Oscar Gonzales (Telefonica)
Henry Yu (Huawei)
Jiang Sun (China Mobile)

## Slide 2: Major Updates Since IETF 115
Separated the data model for network slice topology from the OTN slicing model
  To reflect the WG consensus from IETF-115 that the topology construct is technology-agnostic and applies to any network slice
  The technology-agnostic network slice topology model was proposed in draft-liu-teas-transport-network-slice-yang
OTN slicing augments the network slice topology model with additional OTN technology-specific SLO/SLE arguments
Attributes adjustment
  Removed some SLO/SLE attributes, e.g. periodicity, that are inherited from 5G and are not applicable to OTN slicing
  Moved explicit path references under the steering-constraints in the Network Slice Service model
Text description was updated accordingly

## Slide 3: Updated Model Relationships
ietf-network-slice-service
ietf-transport-network-slice
(w/ topology)
ietf-otn-slice
augments
augments
This draft
draft-ietf-teas-network-slice-nbi
OLD
ietf-network-slice-service
ietf-transport-network-slice
(w/o topology)
ietf-otn-slice
augments
augments
This draft
draft-ietf-teas-network-slice-nbi
NEW
ietf-network-slice-topology
references
augments

## Slide 4: Open Issue - Model Dependencies between WG & non-WG drafts
ietf-otn-slice (WG adopted) depends on ietf-network-slice-topology which is still in I.D. state
  Option 1 : TEAS WG to adopt ietf-network-slice-topology
  Option 2 : create new I.D. for OTN augments for ietf-network-slice-topology
  Option 3 : progress ietf-otn-slice in phases: phase 1 for connectivity only and phase 2 for connectivity + topology
ietf-network-slice-service
ietf-transport-network-slice
(w/o topology)
ietf-otn-slice
augments
augments
This draft
draft-ietf-teas-network-slice-nbi
ietf-network-slice-topology
references
augments
otn-slice-topo

## Slide 5: Open Issue – Can we merge ietf-transport-network-slice with ietf-network-slice-service?
ietf-transport-network-slice contains generic SLO/SLEs that may be applicable to generic network slicing as well. The ietf-transport-network-slice can be eliminated in all if agreed to merge
  …/ietf-nss:steering-constraints:
  +--rw disjointness? te-types:te-path-disjointness
  …/ietf-nss:custom/ietf-nss:service-slo-sle-policy:
  +--rw optimization-criterion? Identityref
  +--rw resize-requirement? identityref
  +--rw service-info? string
  …/ietf-nss:steering-constraints/ietf-nss:path-constraints:
  +--rw topology-id? -> /nw:networks/network/network-id
  +--rw explicit-path* [tp-id]
  +--rw tp-id -> /nw:networks/network/node/nt:termination-point/tp-id

## Slide 6: Next Steps
Address open issues
Continue working with draft-ietf-teas-ietf-network-slice-nbi-yang to align the two models
Add a few examples for various types of OTN slices which combines the use of network-slice-nbi and otn-slice
* GitHub Repo
  https://github.com/ietf-ccamp-wg/ietf-ccamp-yang-otn-slicing
* CCAMP Weekly Call: Thu 10-11am EST
  https://mailarchive.ietf.org/arch/msg/ccamp/Dr3HWPlmP9LyA6NmabWJvx7hWIc/

## Slide 7
Thank You!