## Slide 1: Framework and Data Model for OTN Network Slicing
Co-authors:
Aihua Guo (Futurewei)
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Luis M. Contreras (Telefonica)
Yunbin Xu (CAICT)
Yang Zhao (China Mobile)
Xufeng Liu (IBM Corporation)
draft-ietf-ccamp-yang-otn-slicing-02
Contributors:
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Victor Lopez(Nokia)
Dieter Beller (Nokia)
Oscar Gonzales (Telefonica)
Henry Yu (Huawei)
Jiang Sun (China Mobile)

## Slide 2: Updates Since IETF 113
YANG Model Updates
  Rebased ietf-transport-network-slice.yang by augmenting the model defined in draft-ietf-teas-ietf-network-slice-nbi-yang-02
  Renamed “ietf-otn-slice” to “ietf-otn-slice-mpi”
    “ietf-otn-slice” is reserved for the NBI model
ietf-network-slice-service
ietf-transport-network-slice
ietf-otn-slice
augments
augments
Text Updates
  Added a section to describe OTN slice realization with NRP (Network Resource Partition)
  Other cosmetic updates
This draft
draft-ietf-teas-network-slice-nbi

## Slide 3: Use of NRP for OTN Slicing
NRP can be used to address scalability issues mostly occurred in packet networks and reduce complexity in the realization of slices
NRP is internal construct to a network slice controller, but may be pushed to underlying SDN controller or control plane through MPI to facilitate the realization
For OTN and other transport networks (MW, L0, etc.) resources are much coarse granular
  Use of NRP is optional but still has its benefits for e.g. resource-based slicing
  Evolving OTN data plane technologies may face similar scalability issues.
    E.g. sub-1G OTN

## Slide 4: Realizing OTN Slices with NRP
For connectivity-based OTN slices, a connection within an OTN slice can be realized by an OTN tunnel in the underlay topology. Resources are reserved by the tunnel, thus use of NRP is optional in this case.
For resource-based OTN slices, the OTN-SC may choose to map an OTN slice directly onto the underlay TE topology
  Resources need to be colored in the underlay topology
  A connection created within the slice needs to be specified with colors
Alternatively, the OTN-SC can create NRP topologies for resource reservation.
  OTN slice topology: NRP topology = 1: 1
  No need for coloring
  NRP topologies are pushed to subtended MDSC/PNC through the MPI

## Slide 5: YANG Model Updates
ietf-transport-network-slice.yang now augments ietf-network-slice-services.yang
  Added list of network topologies to support resource-based slicing
  Introduced common SLO grouping for slices with transport network technologies
  Added path references to each connectivity construct of a slice

## Slide 6: Open Issue: How to define technology-specific attributes?
Opaque vs. explicit definition of attributes for e.g. SLO/SLE
  Is it the best way for using opaque definition of (key, value) pairs to define technology-specific attributes?
    May not capture complex attribute structures
    Unable to be auto/explicitly validated with YANG
    Implementation agreements are required in addition to the YANG model
For OTN Slicing we intend to define explicit, technology-specific attributes and not use the opaque definition

## Slide 7: Open Issue: Defining multiple MPI Interface Models?
OTN-SC is flexible in choosing different MPI interfaces for realizing a slice. Use of NRP is optional.
Is it necessary for a standard draft to include multiple optional MPI models? Currently,
  ietf-otn-slice-mpi.yang uses coloring
  New MPI model is needed if using NRP
    Augments the TE topology model (RFC8795) with new topology type = NRP

## Slide 8: Next Steps
Address open issues
Continue working with draft-ietf-teas-ietf-network-slice-nbi-yang-02 to align the two models
Define OTN technology-specific model based on ietf-transport-network-slice (which augments ietf-network-slice-service)
  Technology-specific SLO/SLE for OTN
  Support both connection-based and resource-based slicing
  Support multi technology links (non-OTN access links and OTN links)
* GitHub Repo
  https://github.com/ietf-ccamp-wg/ietf-ccamp-yang-otn-slicing
* CCAMP Weekly Call: Thu 10-11am EST
  https://mailarchive.ietf.org/arch/msg/ccamp/Dr3HWPlmP9LyA6NmabWJvx7hWIc/

## Slide 9
Thank You!